## Slide 1
DIGITAL LOGIC DESIGN PROJECT
UART Transmitter
A Modular, FSM-Driven Serial Transmitter in Verilog
1 0 1 0 0 1 0 1
Serializer • Parity Generator • Output Mux • Control FSM

## Slide 2
OVERVIEW
What We'll Cover
01
01
Protocol Basics
How UART frames data over a single serial wire
02
02
System Architecture
Top-level module and signal interconnect
03
03
Module Deep-Dive
Serializer, parity generator, and output mux
04
04
Control FSM
The state machine that sequences every bit
05
05
Verification
Testbench strategy and simulation results
06
06
Conclusion
Takeaways and possible extensions
UART TRANSMITTER — RTL DESIGN
2

## Slide 3
PROTOCOL
How a UART Frame Is Built
UART (Universal Asynchronous Receiver/Transmitter) sends data one bit at a time over a single wire, with no shared clock between sender and receiver. Timing is agreed on in advance, and every frame follows the same fixed shape.
IDLE
Line high
START
1 bit · 0
DATA
8 bits · LSB first
PARITY
1 bit · optional
STOP
1 bit · 1
IDLE
Line high
Total frame length: 10–11 bits per byte, depending on whether parity is enabled.
Idle High The line rests at logic 1 between frames — this design's mux drives 1 by default (sel = 2'b11).
Start Bit A falling edge to 0 tells the receiver a new byte is coming and syncs its sample clock.
LSB-First The serializer shifts p_data right, so bit 0 is transmitted before bit 7.
UART TRANSMITTER — RTL DESIGN
3

## Slide 4
ARCHITECTURE
System Block Diagram
uart_tx_top
serializer
Parallel-to-serial
shift register
parity
Even / odd
parity generator
fsm
Sequencing &
control logic
mux
4:1 output
select
load_en / shift_en / sel (control signals)
ser_data
parity_out
tx_out
Inputs: clk, rst, valid_in, p_data[7:0], parity_en, parity_bit
Outputs: tx_out (serial line), busy (transmit-in-progress flag)
UART TRANSMITTER — RTL DESIGN
4

## Slide 5
MODULE DEEP-DIVE
Control FSM — the Sequencer
A 5-state Moore-ish machine drives every other block. It asserts load_en to latch new data, shift_en to advance the serializer, sel to steer the mux, and busy so the sender knows when the line is free.
STATE
KEY OUTPUTS
TRANSITION
S0 (Idle)
sel=11, busy=0
valid_in → load_en=1, go to START
START
sel=00 (drive 0)
always → DATA
DATA
sel=01, shift_en=1
loop 8x, then → PARITY or STOP
PARITY
sel=10 (drive parity)
always → STOP
STOP
sel=11 (drive 1)
always → S0
S0
START
DATA
PARITY
STOP
×8
UART TRANSMITTER — RTL DESIGN
5

## Slide 6
MODULE DEEP-DIVE
Serializer & Parity Generator
S
Serializer
An 8-bit shift register performs parallel-to-serial conversion. load_en captures p_data in parallel; shift_en shifts it right one bit per DATA-state clock, exposing bit 0 on ser_data.
1
0
1
0
0
1
0
1
bit 7 ← ................................ → bit 0 (out)
shift_en: shift right each cycle
assign ser_data = shift_reg[0];
P
Parity Generator
A combinational XOR reduction (^data) checks the number of 1s in p_data. parity_bit selects even (0) or odd (1) parity; parity_en gates the whole feature off when not needed.
p_data
^data
parity_bit
parity_out
1010_0101
0
0 (even)
0
0011_1100
0
1 (odd)
1
Note: this design's condition treats parity_bit=0 as even parity and parity_bit=1 as odd parity.
UART TRANSMITTER — RTL DESIGN
6

## Slide 7
MODULE DEEP-DIVE
Output Mux — Building the Line
The mux is the last stop before tx_out. On every clock the FSM's sel signal chooses which internal source drives the physical wire — this is what actually assembles start, data, parity, and stop bits into one continuous stream.
sel
Output driven
Meaning
2'b00
0
START bit
2'b01
data (ser_data)
DATA bit stream
2'b10
parity_out
PARITY bit
2'b11
1
STOP bit / IDLE
0
data
parity_out
1
MUX
4:1
tx_out
sel[1:0]
UART TRANSMITTER — RTL DESIGN
7

## Slide 8
SIGNAL FLOW
Timing Diagram — One Transmitted Byte
Example from simulation: p_data = 8'b1010_0101, parity_en = 1, parity_bit = 0 (even) → parity_out = 0
state / sel
START
D0
D1
D2
D3
D4
D5
D6
D7
PAR
STOP
tx_out
0
1
0
1
0
0
1
0
1
0
1
Because FSM signals are combinational (Mealy-style outputs), sel changes as soon as the state changes, and the mux immediately routes the correct source onto tx_out — producing a clean, glitch-free bitstream.
UART TRANSMITTER — RTL DESIGN
8

## Slide 9
VERIFICATION
Testbench Strategy
uart_tx_tb.v drives uart_tx_top with a free-running clock and applies five back-to-back byte transfers, waiting on the busy flag between them to confirm the FSM returns to idle correctly.
#
p_data
parity_en
parity_bit
Purpose
1
1010_0101
1
0 (even)
Baseline framed byte w/ even parity
2
0011_1100
1
1 (odd)
Same path, odd parity selected
3
1111_1111
0
–
Parity disabled → skip PARITY state
4
0101_0101
1
0 (even)
Alternating pattern, even parity
5
1100_1100
0
–
Back-to-back transfer, no gap tested
✓
busy asserts the cycle after valid_in — confirms handshake timing
✓
tx_out matches expected frame for every vector, incl. parity-disabled path
✓
busy de-asserts exactly at STOP → S0, confirming clean re-idle
UART TRANSMITTER — RTL DESIGN
9

## Slide 10
VERIFICATION
Simulation Results
ModelSim · uart_tx.vcd
clk
rst
valid_in
p_data
busy
tx_out
Representative capture — full signal trace available in vsim.wlf
Key Findings
✓
All 5 testbench vectors produced the expected tx_out bitstream, matching hand-computed frames.
✓
busy correctly frames each transfer — asserted from load through STOP, low only when idle.
✓
Parity logic verified for both even (parity_bit=0) and odd (parity_bit=1) settings.
✓
Disabling parity_en correctly skips the PARITY state, shortening the frame by one bit.
UART TRANSMITTER — RTL DESIGN
10

## Slide 11
CONCLUSION
Takeaways & Next Steps
Takeaways
Clean separation of concerns: FSM controls, datapath modules execute.
sel-driven mux makes the frame format easy to extend or reconfigure.
Fully synchronous design with a single always-block FSM core.
Possible Extensions
Add a matching UART receiver (RX) with baud-rate sampling.
Insert a baud-rate generator to decouple bit time from clk.
Add a TX FIFO to queue multiple bytes without stalling.
Thank you — questions welcome.
UART TRANSMITTER — RTL DESIGN
11